## Slide 1
Forms and Bindings
in Practice
W
W
,
hat is
oT
Notes: In the previous tutorial, we explored Interaction Affordances — properties, actions, and events — and how they describe what a Thing can do. In this video, we will focus on the next important question: How do those interactions actually happen over the network?

## Slide 2
Protocol Bindings in Practice
"href": "https://..."
"op": "readProperty"
HTTP
Notes: Now that we understand the structure of forms, let's see how protocol bindings work in practice. When you want to write a Consumer application, you don't need any prior knowledge about the protocol being used. Instead, the Consumer reads the Thing Description, looks at the available forms, and selects one it understands.
We will now quickly show how forms can look and what they mean for the following protocols: HTTP, CoAP, MQTT, and Modbus. Let's revisit our smart coffee machine example from the last video and fill out the forms for our interaction affordances so far.

## Slide 3
Protocol Bindings in Practice
"href": "https://..."
"op": "readProperty"
HTTP
Consumer
Thing
HTTP
HTTP
CoAP
MQTT
Notes: Now that we understand the structure of forms, let's see how protocol bindings work in practice. When you want to write a Consumer application, you don't need any prior knowledge about the protocol being used. Instead, the Consumer reads the Thing Description, looks at the available forms, and selects one it understands.
We will now quickly show how forms can look and what they mean for the following protocols: HTTP, CoAP, MQTT, and Modbus. Let's revisit our smart coffee machine example from the last video and fill out the forms for our interaction affordances so far.

## Slide 4
Protocol Bindings in Practice
"href": "https://..."
"op": "readProperty"
HTTP
Consumer
Thing
HTTP
HTTP
CoAP
MQTT
Notes: Now that we understand the structure of forms, let's see how protocol bindings work in practice. When you want to write a Consumer application, you don't need any prior knowledge about the protocol being used. Instead, the Consumer reads the Thing Description, looks at the available forms, and selects one it understands.

## Slide 5
Protocol Bindings in Practice
HTTP
CoAP
MQTT
Modbus

## Slide 6
Consumer
Thing
HТTP
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
"properties": {
"coffeeBeansLeft": {
"title": "Remaining Coffee Beans",
"description": "Amount of remaining coffee beans in grams",
"type": "number",
"readOnly": true,
Notes: First, we want the Consumer to perform the `readProperty` operation on `coffeeBeansLeft` so we can get the remaining amount of coffee beans.

## Slide 7
Consumer
Thing
HТTP
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
Notes: To achieve this, the Consumer reads the form and translates it into a network request. The `href` tells it the address and that HTTP is the protocol. Then the `htv:methodName` field says to use a `GET` request and the `contentType` tells it to expect a JSON in return. So the Consumer sends the following request:

## Slide 8
Consumer
Thing
HТTP
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
► HTTP REQUEST
Notes: To achieve this, the Consumer reads the form and translates it into a network request. The `href` tells it the address and that HTTP is the protocol. Then the `htv:methodName` field says to use a `GET` request and the `contentType` tells it to expect a JSON in return. So the Consumer sends the following request:

## Slide 9
Consumer
Thing
HТTP
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
► HTTP REQUEST
GET /properties/coffeeBeansLeft HTTP/1.1
Host: coffee.example.com
Accept: application/json
Notes: To achieve this, the Consumer reads the form and translates it into a network request. The `href` tells it the address and that HTTP is the protocol. Then the `htv:methodName` field says to use a `GET` request and the `contentType` tells it to expect a JSON in return. So the Consumer sends the following request:

## Slide 10
Consumer
Thing
HТTP
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
► HTTP REQUEST
GET /properties/coffeeBeansLeft HTTP/1.1
Host: coffee.example.com
Accept: application/json
Notes: To achieve this, the Consumer reads the form and translates it into a network request. The `href` tells it the address and that HTTP is the protocol. Then the `htv:methodName` field says to use a `GET` request and the `contentType` tells it to expect a JSON in return. So the Consumer sends the following request:

## Slide 11
Consumer
Thing
HТTP
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
► HTTP REQUEST
GET /properties/coffeeBeansLeft HTTP/1.1
Host: coffee.example.com
Accept: application/json
Notes: To achieve this, the Consumer reads the form and translates it into a network request. The `href` tells it the address and that HTTP is the protocol. Then the `htv:methodName` field says to use a `GET` request and the `contentType` tells it to expect a JSON in return. So the Consumer sends the following request:

## Slide 12
Consumer
Thing
HТTP
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
Request
► HTTP REQUEST
GET /properties/coffeeBeansLeft HTTP/1.1
Host: coffee.example.com
Accept: application/json
Notes: To achieve this, the Consumer reads the form and translates it into a network request. The `href` tells it the address and that HTTP is the protocol. Then the `htv:methodName` field says to use a `GET` request and the `contentType` tells it to expect a JSON in return. So the Consumer sends the following request:

## Slide 13
Consumer
Thing
HТTP
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
► HTTP REQUEST
GET /properties/coffeeBeansLeft HTTP/1.1
Host: coffee.example.com
Accept: application/json
HTTP/1.1 200 OK
Content-Type: application/json
Payload: 320
◄ RESPONSE
Response
Notes: The Thing receives this, reads its internal sensor, and responds:

## Slide 14
Consumer
Thing
HТTP
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
► HTTP REQUEST
GET /properties/coffeeBeansLeft HTTP/1.1
Host: coffee.example.com
Accept: application/json
HTTP/1.1 200 OK
Content-Type: application/json
Payload: 320
◄ RESPONSE
Response
...
"type": "number",
...
Notes: The Consumer parses the JSON body - a single number, exactly as the coffeeBeansLeft data schema ("type": "number") declared - and now has the value of 320 grams. The form told it how to fetch; the data schema told it what shape to expect.

## Slide 15
Consumer
Thing
HТTP
...
"properties": {
"coffeeBeansLeft": {
"title": "Remaining Coffee Beans",
"description": "Amount of remaining coffee beans in grams",
"type": "number",
"readOnly": true,
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
...
HTTP
Notes: Here, the form tells the Consumer that it can read the property `coffeeBeansLeft` using HTTP and expects a JSON response. The HTTP method is explicitly defined using `htv:methodName` with the value `GET`, so the Consumer knows exactly which HTTP request method to use.

## Slide 16
Consumer
Thing
HТTP
...
"properties": {
"coffeeBeansLeft": {
"title": "Remaining Coffee Beans",
"description": "Amount of remaining coffee beans in grams",
"type": "number",
"readOnly": true,
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
...
HTTP
Notes: Here, the form tells the Consumer that it can read the property `coffeeBeansLeft` using HTTP and expects a JSON response. The HTTP method is explicitly defined using `htv:methodName` with the value `GET`, so the Consumer knows exactly which HTTP request method to use.

## Slide 17
Consumer
Thing
HТTP
...
"properties": {
"coffeeBeansLeft": {
"title": "Remaining Coffee Beans",
"description": "Amount of remaining coffee beans in grams",
"type": "number",
"readOnly": true,
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
...
JSON
Notes: Here, the form tells the Consumer that it can read the property `coffeeBeansLeft` using HTTP and expects a JSON response. The HTTP method is explicitly defined using `htv:methodName` with the value `GET`, so the Consumer knows exactly which HTTP request method to use.

## Slide 18
Consumer
Thing
HТTP
...
"properties": {
"coffeeBeansLeft": {
"title": "Remaining Coffee Beans",
"description": "Amount of remaining coffee beans in grams",
"type": "number",
"readOnly": true,
"forms": [
{
"href": "https://coffee.example.com/properties/coffeeBeansLeft",
"op": "readproperty",
"contentType": "application/json",
"htv:methodName": "GET"
}
]
...
HTTP GET
Notes: Here, the form tells the Consumer that it can read the property `coffeeBeansLeft` using HTTP and expects a JSON response. The HTTP method is explicitly defined using `htv:methodName` with the value `GET`, so the Consumer knows exactly which HTTP request method to use.

## Slide 19
Consumer
Thing
CoAP
"actions": {
"brewCoffee": {
"title": "Brew Coffee",
"description": "Starts brewing a cup of coffee",
"input": {
"type": "object",
"properties": {
"size": {
"type": "string",
"enum": ["small", "medium", "large"]
}
}
},
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "application/cbor",
"cov:method": "POST"
}
]
Notes: Now the Consumer wants to invoke the `brewCoffee` action.

## Slide 20
Consumer
Thing
CoAP
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "application/cbor",
"cov:method": "POST"
}
]
Notes: The Consumer reads this form just like before - but now `href` starts with `coap://`, so it knows to use CoAP instead of HTTP. The `cov:method` field says `POST`. The contentType is application/cbor, so this time the Consumer encodes the action input in CBOR.
The resulting CoAP message looks something like this:

## Slide 21
Consumer
Thing
CoAP
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "application/cbor",
"cov:method": "POST"
}
]
► CoAP REQUEST
Notes: The Consumer reads this form just like before - but now `href` starts with `coap://`, so it knows to use CoAP instead of HTTP. The `cov:method` field says `POST`. The contentType is application/cbor, so this time the Consumer encodes the action input in CBOR.
The resulting CoAP message looks something like this:

## Slide 22
Consumer
Thing
CoAP
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "application/cbor",
"cov:method": "POST"
}
]
► CoAP REQUEST
CoAP POST coap://coffee.example.com/actions/brewCoffee
Token: 0x4a2b
Content-Format: 60 (= application/cbor)
Payload (CBOR): a1 64 73 69 7a 65 66 6d 65 64 69 75 6d
decoded: { "size": "medium" }
Notes: The Consumer reads this form just like before - but now `href` starts with `coap://`, so it knows to use CoAP instead of HTTP. The `cov:method` field says `POST`. The contentType is application/cbor, so this time the Consumer encodes the action input in CBOR.
The resulting CoAP message looks something like this:

## Slide 23
Consumer
Thing
CoAP
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "application/cbor",
"cov:method": "POST"
}
]
► CoAP REQUEST
CoAP POST coap://coffee.example.com/actions/brewCoffee
Token: 0x4a2b
Content-Format: 60 (= application/cbor)
Payload (CBOR): a1 64 73 69 7a 65 66 6d 65 64 69 75 6d
decoded: { "size": "medium" }
Notes: The Consumer reads this form just like before - but now `href` starts with `coap://`, so it knows to use CoAP instead of HTTP. The `cov:method` field says `POST`. The contentType is application/cbor, so this time the Consumer encodes the action input in CBOR.
The resulting CoAP message looks something like this:

## Slide 24
Consumer
Thing
CoAP
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "application/cbor",
"cov:method": "POST"
}
]
► CoAP REQUEST
CoAP POST coap://coffee.example.com/actions/brewCoffee
Token: 0x4a2b
Content-Format: 60 (= application/cbor)
Payload (CBOR): a1 64 73 69 7a 65 66 6d 65 64 69 75 6d
decoded: { "size": "medium" }
Notes: The Consumer reads this form just like before - but now `href` starts with `coap://`, so it knows to use CoAP instead of HTTP. The `cov:method` field says `POST`. The contentType is application/cbor, so this time the Consumer encodes the action input for a medium sized coffee in CBOR.
The resulting CoAP message looks something like this:

## Slide 25
Consumer
Thing
CoAP
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "application/cbor",
"cov:method": "POST"
}
]
► CoAP REQUEST
CoAP POST coap://coffee.example.com/actions/brewCoffee
Token: 0x4a2b
Content-Format: 60 (= application/cbor)
Payload (CBOR): a1 64 73 69 7a 65 66 6d 65 64 69 75 6d
decoded: { "size": "medium" }
Request
Notes: The Thing receives the message and sends back a CoAP response with code `2.04 Changed`, confirming the action was accepted. From the Consumer's perspective, this was identical to invoking the HTTP action - it performed an invokeaction operation and got a success response. The fact that it used CoAP instead of HTTP, or CBOR instead of JSON, was determined entirely by what was written in the form.

## Slide 26
Consumer
Thing
CoAP
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "application/cbor",
"cov:method": "POST"
}
]
► CoAP REQUEST
CoAP POST coap://coffee.example.com/actions/brewCoffee
Token: 0x4a2b
Content-Format: 60 (= application/cbor)
Payload (CBOR): a1 64 73 69 7a 65 66 6d 65 64 69 75 6d
decoded: { "size": "medium" }
CoAP ACK 2.04 Changed
Token: 0x4a2b
(no payload body)
◄ RESPONSE
Response
Notes: The Thing receives the message and sends back a CoAP response with code `2.04 Changed`, confirming the action was accepted. From the Consumer's perspective, this was identical to invoking the HTTP action - it performed an invokeaction operation and got a success response. The fact that it used CoAP instead of HTTP, or CBOR instead of JSON, was determined entirely by what was written in the form.

## Slide 27
Consumer
Thing
CoAP
...
"actions": {
"brewCoffee": {
"title": "Brew Coffee",
"description": "Starts brewing a cup of coffee",
"input": {
"type": "object",
"properties": {
"size": {
"type": "string",
"enum": ["small", "medium", "large"]
}
}
},
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "text/plain",
"cov:method": "POST"
}
]
...
Notes: Let's use CoAP to invoke the `brewCoffee` action: This time, the form uses a `coap://` URI to indicate CoAP instead of HTTP. The `cov:method` field explicitly specifies the CoAP request method — in this case `POST` — which tells the Consumer how to invoke the action at the protocol level. From the Consumer's perspective, invoking the action works conceptually the same as with HTTP — the only difference is the underlying protocol, which is optimized for constrained devices.

## Slide 28
Consumer
Thing
CoAP
...
"actions": {
"brewCoffee": {
"title": "Brew Coffee",
"description": "Starts brewing a cup of coffee",
"input": {
"type": "object",
"properties": {
"size": {
"type": "string",
"enum": ["small", "medium", "large"]
}
}
},
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "text/plain",
"cov:method": "POST"
}
]
...
CoAP
Notes: Let's use CoAP to invoke the `brewCoffee` action: This time, the form uses a `coap://` URI to indicate CoAP instead of HTTP. The `cov:method` field explicitly specifies the CoAP request method — in this case `POST` — which tells the Consumer how to invoke the action at the protocol level. From the Consumer's perspective, invoking the action works conceptually the same as with HTTP — the only difference is the underlying protocol, which is optimized for constrained devices.

## Slide 29
Consumer
Thing
CoAP
...
"actions": {
"brewCoffee": {
"title": "Brew Coffee",
"description": "Starts brewing a cup of coffee",
"input": {
"type": "object",
"properties": {
"size": {
"type": "string",
"enum": ["small", "medium", "large"]
}
}
},
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "text/plain",
"cov:method": "POST"
}
]
...
CoAP
POST
Notes: Let's use CoAP to invoke the `brewCoffee` action: This time, the form uses a `coap://` URI to indicate CoAP instead of HTTP. The `cov:method` field explicitly specifies the CoAP request method — in this case `POST` — which tells the Consumer how to invoke the action at the protocol level. From the Consumer's perspective, invoking the action works conceptually the same as with HTTP — the only difference is the underlying protocol, which is optimized for constrained devices.

## Slide 30
Consumer
Thing
CoAP
...
"actions": {
"brewCoffee": {
"title": "Brew Coffee",
"description": "Starts brewing a cup of coffee",
"input": {
"type": "object",
"properties": {
"size": {
"type": "string",
"enum": ["small", "medium", "large"]
}
}
},
"forms": [
{
"href": "coap://coffee.example.com/actions/brewCoffee",
"op": "invokeaction",
"contentType": "text/plain",
"cov:method": "POST"
}
]
...
Text
Notes: Let's use CoAP to invoke the `brewCoffee` action: This time, the form uses a `coap://` URI to indicate CoAP instead of HTTP. The `cov:method` field explicitly specifies the CoAP request method — in this case `POST` — which tells the Consumer how to invoke the action at the protocol level. From the Consumer's perspective, invoking the action works conceptually the same as with HTTP — the only difference is the underlying protocol, which is optimized for constrained devices.

## Slide 31
Consumer
Thing
MQTT
"events": {
"lowOnWater": {
"title": "Low Water Level",
"data": {
"type": "number",
"description": "Remaining water level in milliliters"
},
Broker
"forms": [
{
"href": "mqtt://broker.example.com:1883,
"op": "subscribeevent",
"mqv:filter": "coffee/events/lowOnWater",
"mqv:qos": "1",
"contentType": "text/plain"
}
]
Notes: For the lowOnWater event, the form looks like this:

## Slide 32
Consumer
Thing
MQTT
Broker
"forms": [
{
"href": "mqtt://broker.example.com:1883,
"op": "subscribeevent",
"mqv:filter": "coffee/events/lowOnWater",
"mqv:qos": "1",
"contentType": "text/plain"
}
]
► CONSUMER CONTROL PACKET
Notes: The `op` field is `subscribeevent`, which tells the Consumer it needs to listen rather than request. The href points to an MQTT broker and includes the topic — `coffee/events/lowOnWater` — that the Consumer should subscribe to. So the Consumer connects to the broker and sends:

## Slide 33
Consumer
Thing
MQTT
Broker
"forms": [
{
"href": "mqtt://broker.example.com:1883,
"op": "subscribeevent",
"mqv:filter": "coffee/events/lowOnWater",
"mqv:qos": "1",
"contentType": "text/plain"
}
]
► CONSUMER CONTROL PACKET
SUBSCRIBE
Topic: coffee/events/lowOnWater
QoS: 1
Notes: The `op` field is `subscribeevent`, which tells the Consumer it needs to listen rather than request. The `href` points to the MQTT broker, and the `mqv:filter` term gives the topic filter - `coffee/events/lowOnWater` - that the Consumer should subscribe to. The `mqv:qos` term requests QoS level 1, MQTT's at-least-once delivery. So the Consumer connects to the broker and sends:

## Slide 34
Consumer
Thing
MQTT
Broker
"forms": [
{
"href": "mqtt://broker.example.com:1883,
"op": "subscribeevent",
"mqv:filter": "coffee/events/lowOnWater",
"mqv:qos": "1",
"contentType": "text/plain"
}
]
► CONSUMER CONTROL PACKET
SUBSCRIBE
Topic: coffee/events/lowOnWater
Notes: The `op` field is `subscribeevent`, which tells the Consumer it needs to listen rather than request. The `href` points to the MQTT broker, and the `mqv:filter` term gives the topic filter - `coffee/events/lowOnWater` - that the Consumer should subscribe to. The `mqv:qos` term requests QoS level 1, MQTT's at-least-once delivery. So the Consumer connects to the broker and sends:

## Slide 35
Consumer
Thing
MQTT
Broker
"forms": [
{
"href": "mqtt://broker.example.com:1883,
"op": "subscribeevent",
"mqv:filter": "coffee/events/lowOnWater",
"mqv:qos": "1",
"contentType": "text/plain"
}
]
► CONSUMER CONTROL PACKET
SUBSCRIBE
Topic: coffee/events/lowOnWater
PUBLISH
Topic: coffee/events/lowOnWater
QoS: 1
Payload: 50
◄ THING CONTROL PACKET
Response
Response
Notes: The broker forwards this to the Consumer. The Consumer receives the message, parses the text as declared by `contentType`, and now has the event data: 50 milliliters remaining.
What's important here is that the WoT operation `subscribeevent` naturally maps to MQTT's publish/subscribe model. The Consumer didn't need to know it was MQTT — it simply performed a `subscribeevent` operation, and the form told it exactly how to do that: connect to this broker, subscribe to this topic and expect a plain text response.

## Slide 36
Consumer
Thing
MQTT
Broker
"forms": [
{
"href": "mqtt://broker.example.com:1883,
"op": "subscribeevent",
"mqv:filter": "coffee/events/lowOnWater",
"mqv:qos": "1",
"contentType": "text/plain"
}
]
► CONSUMER CONTROL PACKET
SUBSCRIBE
Topic: coffee/events/lowOnWater
PUBLISH
Topic: coffee/events/lowOnWater
QoS: 1
Payload: 50
◄ THING CONTROL PACKET
Notes: The broker forwards this to the Consumer. The Consumer receives the message, parses the text as declared by `contentType`, and now has the event data: 50 milliliters remaining.
What's important here is that the WoT operation `subscribeevent` naturally maps to MQTT's publish/subscribe model. The Consumer didn't need to know it was MQTT — it simply performed a `subscribeevent` operation, and the form told it exactly how to do that: connect to this broker, subscribe to this topic and expect a plain text response.

## Slide 37
Consumer
Thing
MQTT
...
"events": {
"lowOnWater": {
"title": "Low Water Level",
"data": {
"type": "number",
"description": "Remaining water level in milliliters"
},
"forms": [
{
"href": "mqtt://broker.example.com/coffee/events/lowOnWater",
"op": "subscribeevent",
"contentType": "application/json"
}
]
...
Broker
Notes: Here, the href points to an MQTT broker and topic. The Consumer connects to the MQTT broker, subscribes to the specified topic, and receives event data asynchronously from the broker whenever the event occurs. The Thing publishes event messages to the same topic, and the MQTT broker delivers those published messages to all subscribed Consumers.

## Slide 38
Consumer
Thing
MQTT
...
"events": {
"lowOnWater": {
"title": "Low Water Level",
"data": {
"type": "number",
"description": "Remaining water level in milliliters"
},
"forms": [
{
"href": "mqtt://broker.example.com/coffee/events/lowOnWater",
"op": "subscribeevent",
"contentType": "application/json"
}
]
...
Broker
Notes: Here, the href points to an MQTT broker and topic. The Consumer connects to the MQTT broker, subscribes to the specified topic, and receives event data asynchronously from the broker whenever the event occurs. The Thing publishes event messages to the same topic, and the MQTT broker delivers those published messages to all subscribed Consumers.

## Slide 39
Consumer
Thing
MQTT
...
"events": {
"lowOnWater": {
"title": "Low Water Level",
"data": {
"type": "number",
"description": "Remaining water level in milliliters"
},
"forms": [
{
"href": "mqtt://broker.example.com/coffee/events/lowOnWater",
"op": "subscribeevent",
"contentType": "application/json"
}
]
...
Broker
JSON
JSON
Notes: Here, the href points to an MQTT broker and topic. The Consumer connects to the MQTT broker, subscribes to the specified topic, and receives event data asynchronously from the broker whenever the event occurs. The Thing publishes event messages to the same topic, and the MQTT broker delivers those published messages to all subscribed Consumers.

## Slide 40
Modbus
Notes: We've now seen three protocols applied to different affordances of our coffee machine. Let's see how we'd adapt it to a completely different kind of protocol: Modbus.

## Slide 41
Consumer
Thing
Modbus
Existing Modbus Systems
Notes: Modbus is a traditional industrial protocol widely used in automation and control systems. While it predates modern web technologies, WoT protocol bindings make it possible to expose Modbus-based devices through a standardized Thing Description. This allows legacy industrial equipment to be integrated into modern web-based systems, without changing the underlying protocol.

## Slide 42
Consumer
Thing
Modbus
Existing Modbus Systems
Notes: Modbus is a traditional industrial protocol widely used in automation and control systems. While it predates modern web technologies, WoT protocol bindings make it possible to expose Modbus-based devices through a standardized Thing Description. This allows legacy industrial equipment to be integrated into modern web-based systems, without changing the underlying protocol.

## Slide 43
Consumer
Thing
Modbus
WoT allows seamless integration of legacy industrial equipment into modern systems.
Notes: Modbus is a traditional industrial protocol widely used in automation and control systems. While it predates modern web technologies, WoT protocol bindings make it possible to expose Modbus-based devices through a standardized Thing Description. This allows legacy industrial equipment to be integrated into modern web-based systems, without changing the underlying protocol.

## Slide 44
Consumer
Thing
Modbus
"base": "modbus+tcp://192.0.2.1:502/1/",
"properties": {
"waterLevel": {
"title": "Water Level",
"type": "integer",
"description": "Current water level in milliliters",
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
Notes: Let's trace how the Consumer translates this form into a Modbus message. The `base` URI gives it the device address and port 502. The /1/ at the end is the Unit ID — the Modbus device identifier on the bus. The `href` value `10003` is the register address. The `modv:function` field says `HoldingRegister`, which can be read or written to, and are typically used to store sensor values like a water level. Putting this all together, the Consumer sends:

## Slide 45
Consumer
Thing
Modbus
"base": "modbus+tcp://192.0.2.1:502/1/",
"properties": {
"waterLevel": {
"title": "Water Level",
"type": "integer",
"description": "Current water level in milliliters",
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
Notes: Let's trace how the Consumer translates this form into a Modbus message. The `base` URI gives it the device address and port 502. The /1/ at the end is the Unit ID — the Modbus device identifier on the bus. The `href` value `10003` is the register address. The `modv:function` field says `HoldingRegister`, which can be read or written to, and are typically used to store sensor values like a water level. Putting this all together, the Consumer sends:

## Slide 46
Consumer
Thing
Modbus
"base": "modbus+tcp://192.0.2.1:502/1/",
"properties": {
"waterLevel": {
"title": "Water Level",
"type": "integer",
"description": "Current water level in milliliters",
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
Notes: Let's trace how the Consumer translates this form into a Modbus message. The `base` URI gives it the device address and port 502. The /1/ at the end is the Unit ID — the Modbus device identifier on the bus. The `href` value `10003` is the register address. The `modv:function` field says `HoldingRegister`, which can be read or written to, and are typically used to store sensor values like a water level. Putting this all together, the Consumer sends:

## Slide 47
Consumer
Thing
Modbus
"base": "modbus+tcp://192.0.2.1:502/1/",
"properties": {
"waterLevel": {
"title": "Water Level",
"type": "integer",
"description": "Current water level in milliliters",
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
Notes: Let's trace how the Consumer translates this form into a Modbus message. The `base` URI gives it the device address and port 502. The /1/ at the end is the Unit ID — the Modbus device identifier on the bus. The `href` value `10003` is the register address. The `modv:function` field says `HoldingRegister`, which can be read or written to, and are typically used to store sensor values like a water level. Putting this all together, the Consumer sends:

## Slide 48
Consumer
Thing
Modbus
"base": "modbus+tcp://192.0.2.1:502/1/",
"properties": {
"waterLevel": {
"title": "Water Level",
"type": "integer",
"description": "Current water level in milliliters",
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
Notes: Let's trace how the Consumer translates this form into a Modbus message. The `base` URI gives it the device address and port 502. The /1/ at the end is the Unit ID — the Modbus device identifier on the bus. The `href` value `10003` is the register address. The `modv:function` field says `HoldingRegister`, which can be read or written to, and are typically used to store sensor values like a water level. Putting this all together, the Consumer sends:

## Slide 49
Consumer
Thing
Modbus
"base": "modbus+tcp://192.0.2.1:502/1/",
"properties": {
"waterLevel": {
"title": "Water Level",
"type": "integer",
"description": "Current water level in milliliters",
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
Notes: Let's trace how the Consumer translates this form into a Modbus message. The `base` URI gives it the device address and port 502. The /1/ at the end is the Unit ID — the Modbus device identifier on the bus. The `href` value `10003` is the register address. The `modv:function` field says `HoldingRegister`, which can be read or written to, and are typically used to store sensor values like a water level. Putting this all together, the Consumer sends:

## Slide 50
Consumer
Thing
Modbus
"base": "modbus+tcp://192.0.2.1:502/1/",
"properties": {
"waterLevel": {
"title": "Water Level",
"type": "integer",
"description": "Current water level in milliliters",
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
Notes: Let's trace how the Consumer translates this form into a Modbus message. The `base` URI gives it the device address and port 502. The /1/ at the end is the Unit ID — the Modbus device identifier on the bus. The `href` value `10003` is the register address. The `modv:function` field says `HoldingRegister`, which can be read or written to, and are typically used to store sensor values like a water level. Putting this all together, the Consumer sends:

## Slide 51
Consumer
Thing
Modbus
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
► REQUEST
Unit ID: 0x01 (from /1/ in base URI)
Function Code: 0x03 (readHoldingRegisters)
Start Address: 40003
Quantity: 0x0001 (read 1 register = 2 bytes)
Request
Notes: The Consumer receives those two bytes and interprets them as a 16-bit big-endian integer: 0x012C = 300. Because the Thing Description specifies that `waterLevel` is an integer, the WoT runtime automatically turns this into the number 300 — the water level in milliliters.

## Slide 52
Consumer
Thing
Modbus
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
► REQUEST
Unit ID: 0x01 (from /1/ in base URI)
Function Code: 0x03 (readHoldingRegisters)
Start Address: 40003
Quantity: 0x0001 (read 1 register = 2 bytes)
Function Code: 0x03
Byte Count: 0x02
Data: 0x01 0x2C (= 300 decimal)
◄ RESPONSE
Response
Notes: The Consumer receives those two bytes and interprets them as a 16-bit big-endian integer: 0x012C = 300. Because the Thing Description specifies that `waterLevel` is an integer, the WoT runtime automatically turns this into the number 300 — the water level in milliliters.

## Slide 53
Consumer
Thing
Modbus
"forms": [
{
"op": "readproperty",
"href": "40003",
"modv:function": "readHoldingRegisters",
"contentType": "application/octet-stream"
}
]
► REQUEST
Unit ID: 0x01 (from /1/ in base URI)
Function Code: 0x03 (readHoldingRegisters)
Start Address: 40003
Quantity: 0x0001 (read 1 register = 2 bytes)
Function Code: 0x03
Byte Count: 0x02
Data: 0x01 0x2C (= 300 decimal)
◄ RESPONSE
Notes: The Consumer receives those two bytes and interprets them as a 16-bit big-endian integer: 0x012C = 300. Because the Thing Description specifies that `waterLevel` is an integer, the WoT runtime automatically turns this into the number 300 — the water level in milliliters.

## Slide 54
Consumer
Thing
Modbus
...
"base": "modbus+tcp://coffee-machine.example.com:502/1/",
"properties": {
"waterTankPresent": {
"title": "Water Tank Present",
"type": "integer",
"description": "Indicates whether the water tank is correctly inserted",
"forms": [
{
"op": "readproperty",
"href": "10003",
"modv:function": "readDiscreteInput",
"contentType": "application/octet-stream"
}
]
...
Notes: For example, our coffee machine has a waterTankPresent property. The form references the Modbus address 10003 and specifies the Modbus function using modv:function with the value readDiscreteInput, which defines the concrete Modbus operation to execute. The contentType is set to application/octet-stream, which means the expected response is a sequence of bytes.
The Consumer implementation itself must support Modbus in order to execute this operation. However, the developer writing the Thing Description — and the user interacting with the Thing — do not need detailed knowledge of Modbus specifics. WoT effectively acts as a semantic and interaction layer on top of Modbus, bridging the gap between industrial systems and web applications.

## Slide 55
Consumer
Thing
Modbus
...
"base": "modbus+tcp://coffee-machine.example.com:502/1/",
"properties": {
"waterTankPresent": {
"title": "Water Tank Present",
"type": "integer",
"description": "Indicates whether the water tank is correctly inserted",
"forms": [
{
"op": "readproperty",
"href": "10003",
"modv:function": "readDiscreteInput",
"contentType": "application/octet-stream"
}
]
...
Notes: For example, our coffee machine has a waterTankPresent property. The form references the Modbus address 10003 and specifies the Modbus function using modv:function with the value readDiscreteInput, which defines the concrete Modbus operation to execute. The contentType is set to application/octet-stream, which means the expected response is a sequence of bytes.
The Consumer implementation itself must support Modbus in order to execute this operation. However, the developer writing the Thing Description — and the user interacting with the Thing — do not need detailed knowledge of Modbus specifics. WoT effectively acts as a semantic and interaction layer on top of Modbus, bridging the gap between industrial systems and web applications.

## Slide 56
Consumer
Thing
Modbus
...
"base": "modbus+tcp://coffee-machine.example.com:502/1/",
"properties": {
"waterTankPresent": {
"title": "Water Tank Present",
"type": "integer",
"description": "Indicates whether the water tank is correctly inserted",
"forms": [
{
"op": "readproperty",
"href": "10003",
"modv:function": "readDiscreteInput",
"contentType": "application/octet-stream"
}
]
...
Notes: For example, our coffee machine has a waterTankPresent property. The form references the Modbus address 10003 and specifies the Modbus function using modv:function with the value readDiscreteInput, which defines the concrete Modbus operation to execute. The contentType is set to application/octet-stream, which means the expected response is a sequence of bytes.
The Consumer implementation itself must support Modbus in order to execute this operation. However, the developer writing the Thing Description — and the user interacting with the Thing — do not need detailed knowledge of Modbus specifics. WoT effectively acts as a semantic and interaction layer on top of Modbus, bridging the gap between industrial systems and web applications.

## Slide 57
Consumer
Thing
Modbus
...
"base": "modbus+tcp://coffee-machine.example.com:502/1/",
"properties": {
"waterTankPresent": {
"title": "Water Tank Present",
"type": "integer",
"description": "Indicates whether the water tank is correctly inserted",
"forms": [
{
"op": "readproperty",
"href": "10003",
"modv:function": "readDiscreteInput",
"contentType": "application/octet-stream"
}
]
...
octet-stream
Notes: For example, our coffee machine has a waterTankPresent property. The form references the Modbus address 10003 and specifies the Modbus function using modv:function with the value readDiscreteInput, which defines the concrete Modbus operation to execute. The contentType is set to application/octet-stream, which means the expected response is a sequence of bytes.
The Consumer implementation itself must support Modbus in order to execute this operation. However, the developer writing the Thing Description — and the user interacting with the Thing — do not need detailed knowledge of Modbus specifics. WoT effectively acts as a semantic and interaction layer on top of Modbus, bridging the gap between industrial systems and web applications.

## Slide 58
Consumer
Thing
Modbus
...
"base": "modbus+tcp://coffee-machine.example.com:502/1/",
"properties": {
"waterTankPresent": {
"title": "Water Tank Present",
"type": "integer",
"description": "Indicates whether the water tank is correctly inserted",
"forms": [
{
"op": "readproperty",
"href": "10003",
"modv:function": "readDiscreteInput",
"contentType": "application/octet-stream"
}
]
...
Modbus
Notes: The Consumer implementation itself must support Modbus in order to execute this operation. However, the developer writing the Thing Description — and the user interacting with the Thing — do not need detailed knowledge of Modbus specifics. WoT effectively acts as a semantic and interaction layer on top of Modbus, bridging the gap between industrial systems and web applications.

## Slide 59
Consumer
Thing
Modbus
...
"base": "modbus+tcp://coffee-machine.example.com:502/1/",
"properties": {
"waterTankPresent": {
"title": "Water Tank Present",
"type": "integer",
"description": "Indicates whether the water tank is correctly inserted",
"forms": [
{
"op": "readproperty",
"href": "10003",
"modv:function": "readDiscreteInput",
"contentType": "application/octet-stream"
}
]
...
Modbus
Notes: The Consumer implementation itself must support Modbus in order to execute this operation. However, the developer writing the Thing Description — and the user interacting with the Thing — do not need detailed knowledge of Modbus specifics. WoT effectively acts as a semantic and interaction layer on top of Modbus, bridging the gap between industrial systems and web applications.

## Slide 60
Summary
Notes: To summarize:
- Protocol bindings define how interactions are executed over the network
- They are expressed using `forms` in the Thing Description
- Different protocols fit different interaction patterns
- WoT unifies them under a single, consistent interaction model

## Slide 61
Summary
Notes: To summarize:
- Protocol bindings define how interactions are executed over the network
- They are expressed using `forms` in the Thing Description
- Different protocols fit different interaction patterns
- WoT unifies them under a single, consistent interaction model

## Slide 62
Summary
Bindings define how interactions are executed over the network.
Notes: To summarize:
- Protocol bindings define how interactions are executed over the network
- They are expressed using `forms` in the Thing Description
- Different protocols fit different interaction patterns
- WoT unifies them under a single, consistent interaction model

## Slide 63
Summary
Bindings define how interactions are executed over the network.
They are expressed using "forms" in the Thing Description.
Notes: To summarize:
- Protocol bindings define how interactions are executed over the network
- They are expressed using `forms` in the Thing Description
- Different protocols fit different interaction patterns
- WoT unifies them under a single, consistent interaction model

## Slide 64
Summary
Bindings define how interactions are executed over the network.
They are expressed using "forms" in the Thing Description.
Different protocols fit different interaction patterns.
Notes: To summarize:
- Protocol bindings define how interactions are executed over the network
- They are expressed using `forms` in the Thing Description
- Different protocols fit different interaction patterns
- WoT unifies them under a single, consistent interaction model

## Slide 65
Summary
Bindings define how interactions are executed over the network.
They are expressed using "forms" in the Thing Description.
Different protocols fit different interaction patterns.
WoT unifies them under a single, consistent interaction model.
Notes: To summarize:
- Protocol bindings define how interactions are executed over the network
- They are expressed using `forms` in the Thing Description
- Different protocols fit different interaction patterns
- WoT unifies them under a single, consistent interaction model

## Slide 66
Next Video
Subscribe to our Channel
Playlist